## Slide 1
1960: Theodore Maiman constructs first ruby laser
Importance:
First Laser Constructed
Study of Population Inversion
Laser Medium Exploration
Lead to/exploration of gas lasers
Applications:
Range Finders
Tattoo Removal
Hair Removal
Holography
Material Strength Examination
Cutting Diamonds!
Population Inversion
How It Works:
Flash tube usually constructed from xenon used to strike ruby.
Synthetic ruby crystal is used as a gain medium, where electrons are excited.
The flashes are very bright and cause electrons to “jump” to higher energy levels.
After population inversion is maintained the electrons then drop to a lower energy and release photons≈ 690nm
The alternating flashing of the xenon flashtube allows the process to continue.
Theodore Maiman (1927-2007)
Methodology:
Maser possibility (Laser we can see) shown.
Thought that Ruby as a medium would require too much energy to produce populated inversion.
Try Ruby by pumping with various light sources.
Found Flashtube to work (so intense it will ignite steel wool).